## Slide 1: IG-RL: Inductive Graph Reinforcement Learning for Massive-Scale Traffic Signal Control
Literature review

## Slide 2: Contents
Motivation
1
2
Methodology
3
Experiment

## Slide 3: 1 Motivation

## Slide 4: 1 Motivation
Fixed network structure

## Slide 5: 1 Motivation
Reinforcement learning to traffic control has strong specification, which hinders transferability and generalization
Fixed network structure

## Slide 6: 1 Motivation
Train a ubiquitous policy which can adapt to new road networks, including topologies and traffic never experienced during training.
1

## Slide 7: 1 Motivation
Lack of careful exploitation on dynamic traffic entities (i.e., vehicle), but limit the idea on fixed upstream-downstream consideration.

## Slide 8: 1 Motivation
Exploit the vehicular data at its finest granularity.
2

## Slide 9: 2 Methodology
  Basic Idea
    Deep Q learning to learn control policy.
    Graph convolution network to introduce consideration on dynamic entities appearing during the control period.

## Slide 10: 2 Methodology
  Basic Idea
    Deep Q learning to learn control policy.
    Graph convolution network to introduce consideration on dynamic entities appearing during the control period.
State features
Action:
switch to next phase or not
Reward: Queue length of different inflow lanes

## Slide 11: 2 Methodology
  Basic Idea
    Deep Q learning to learn control policy.
    Graph convolution network to introduce consideration on dynamic entities appearing during the control period.

## Slide 12: 2 Methodology
  Basic Idea
    Deep Q learning to learn control policy.
    Graph convolution network to introduce consideration on dynamic entities appearing during the control period.
An intersection together with its possible traffic flow dynamic can be represented as nodes in a graph

## Slide 13: 2 Methodology
  Basic Idea
    Deep Q learning to learn control policy.
    Graph convolution network to introduce consideration on dynamic entities appearing during the control period.
Traffic signal controller node

## Slide 14: 2 Methodology
  Basic Idea
    Deep Q learning to learn control policy.
    Graph convolution network to introduce consideration on dynamic entities appearing during the control period.
Traffic signal controller node
Time elapse since last signal control (switch the signal phase)

## Slide 15: 2 Methodology
  Basic Idea
    Deep Q learning to learn control policy.
    Graph convolution network to introduce consideration on dynamic entities appearing during the control period.
Connection node
Is open
Its current open priority
Next open priority

## Slide 16: 2 Methodology
  Basic Idea
    Deep Q learning to learn control policy.
    Graph convolution network to introduce consideration on dynamic entities appearing during the control period.
Lane node
Lane
Number of vehicles
Average speed

## Slide 17: 2 Methodology
  Basic Idea
    Deep Q learning to learn control policy.
    Graph convolution network to introduce consideration on dynamic entities appearing during the control period.
Vehicle node
Current speed
Position on lane

## Slide 18: 2 Methodology
  Basic Idea
    Deep Q learning to learn control policy.
    Graph convolution network to introduce consideration on dynamic entities appearing during the control period.
Vehicle node
Connection node
Traffic signal controller node
Lane node

## Slide 19: 2 Methodology
  Basic Idea
    Deep Q learning to learn control policy.
    Graph convolution network to introduce consideration on dynamic entities appearing during the control period.

## Slide 20: 2 Methodology
  Basic Idea
    Deep Q learning to learn control policy.
    Graph convolution network to introduce consideration on dynamic entities appearing during the control period.
  Multiple GCN layer to produce node embedding.
  For each node, its neighboring nodes can belong to different types.
  Different type of node corresponds to different parameter set.
  The number and feature dimension of the neighboring node is free.

## Slide 21: 2 Methodology
  Basic Idea
    Deep Q learning to learn control policy.
    Graph convolution network to introduce consideration on dynamic entities appearing during the control period.
  There is no additional setting (i.e. Weighted adjacency matrix) to distinguish nodes from the same category, but the feature itself.

## Slide 22: 2 Methodology
  Basic Idea
    Deep Q learning to learn control policy.
    Graph convolution network to introduce consideration on dynamic entities appearing during the control period.
  Add independent gaussian noise to the parameters of network, in order to favor consistent and state-independent policy exploration.

## Slide 23: 3 Experiment
  Set up (Train setting)
    Models
      S-IG-RL-L : Specialized (Train in the scenario for test)
      G-IG-RL-L: General (Train in random scenario)
      G-IG-RL-V: vehicle node considered while ignore lane

## Slide 24: 3 Experiment
  Set up (Train setting)
    Models
      S-IG-RL-L : Specialized (Train in the scenario for test)
      G-IG-RL-L: General (Train in random scenario)
      G-IG-RL-V: vehicle node considered while ignore lane
  Why do not consider both the vehicle and lane node?

## Slide 25: 3 Experiment
  Set up (Train setting)
    Random network structure
      Number of intersections
      Number of edges for each intersection
      Number of lanes per route
    Random traffic flow
      Vehicle trajectory (start lane-immediate lanes-final lane)
    Random training set
      Train in parallel with different random seeds

## Slide 26: 3 Experiment
  Set up (Test setting)
    Same network structure
    Identical demand
      Vehicle trajectory (start lane-immediate lanes-final lane)
    Evaluation
    Baselines
      Fixed time (predefined and constant phases)
      Max moving car heuristic (Switch phases if there are more stopped vehicles than moving vehicles in inbound lanes )
      MARL-IQL (Naïve independent DQN)
Maximum speed of vehicle
Total instantaneous delay at timestep t

## Slide 27: 3 Experiment
  Transferability and Flexibility
Default traffic regime (used in training)
Heavy traffic regime
Trip duration

## Slide 28: 3 Experiment
  Transferability and Flexibility
Default traffic regime (used in training)
Heavy traffic regime
Total delay evolution

## Slide 29: 3 Experiment
  Transferability and Flexibility
Default traffic regime (used in training)
Heavy traffic regime
Differences of Paired Trips Durations (compared to IG-RL-V)

## Slide 30: 3 Experiment
  Transfer and scaling (3971 intersections in Manhattan Island)

## Slide 31: Thank you for watching !